SETTING TOOL HEIGHT

- With MACHINE OFF bring tool down close to part surface using QUILL handle.

- While rotating tool back and forth slowly raise table with KNEE CRANK until tool lightly contacts the part surface. A shim or calibration block can also be used.

- Loosen lock nut on Knee dial and set dial to ZERO mark.

- Raise the Quill to clear the tool from the part.

- Turn the KNEE CRANK to achieve desired cut depth. Clockwise will raise the table increasing the depth of cut.